## Slide 1
EE 5780 Advanced VLSI CAD Project II
Chentao Zhao
Thermal analysis problem in 2D
Solution

## Slide 2
Problem description
Problem detail:
  Heat conduct issue;
  2D dimension problem;
  Solving for static states;
  8X8 elements, 64 unknowns;
Key point:
  Conduction equation;
  3 Reflective boundary;
  Matrix dimension and stamping;

## Slide 3
Equation derivation
Heat conduction PDE equation:
Simplified
Fit for 2D dimension
Fit for steady states problem
Discretization

## Slide 4
Boundary issue
What is the heat performance of the element at the boungdary?
For elements at 20 Celsius side; similar to node connect to constant voltage source.
For the other 3 size. Reflective boundary indicates no heat transfer between these elements to boundary , equivalent to:
  physics, same temperature;
  Mathematically, no heat transfer term ;
term1
term2
term3
term4

## Slide 5
Matrix Dimension
How can we store the problem in matrix?
We scan the element in column sequence .(tricky)
  Reason: the right boundary will be placed at the bottom of the matrix
64 unknown, so we have 64x64 matrix G for heat conductance, 64x1 vector T for element temperature(solution vector); 64 vector I for heat power source(56) and right boundary Temperature(8)
GxT=I ; Then stamping is the only issue left

## Slide 6
Stamping strategy
We Try a 3x3 sample first seeking for the regulation
Regulation can be summarize as below:
  We have 5 kinds of 8x8 basic submatrix element (totally 64), namely Matrix A,B,C,Z,D
  We stamping them separately.
  Then assemble them into G matrix.
  Submatrix Z is all zero matrix, O is unit marix.
  Matrix A B C are all diagonal matrix
  Beautiful strategy due to specific problem.

## Slide 8
Stamping strategy Cont…
Vector I are last step of stamping;
For I (1:56) , the value is the heat power source (we assume the value ourselves)
For I (56:64) , the value is the temperature at the right boundary.
Problem then can be solve by solve the inverse of G and matrix multiply

## Slide 9
Result and Verification

## Slide 10
Result and Verification

## Slide 11
Result and Verification
500W each

## Slide 12
Result and Verification
500W each

## Slide 13
Summery
Need a reasonable heat map of high resolution
For hundreds elements, nice parser to stamping automatically is needed.
For Ten thousands elements, the inverse solver is slow in matlab.
For more , multigrid and literation methods are necessary.